## Slide 1
Lab: BRB 7-022, (410) 706-2173
Staff: flowcore@som.umaryland.edu
Link to Flow Lecture and Resources
Xiaoxuan Fan, PhD
Director
XiaoxuanFan@som.umaryland.edu
UMGCCC Flow Cytometry Shared Service
Karen Underwood, MS
Kunderwood@som.umaryland.edu
Bryan Hahn, BS
BryanHahn@som.umaryland.edu
Notes: 1

## Slide 2
Markers & CDs : Specific proteins on cells that help identify their “lineage”
Rather than rely on “morphology”, use defined MOLECULAR features !!
CD8
Marker:
e.g. CD4
Mixture of cells
+
Dye
Dye
Anti-CD4 mAb
Anti-CD8 mAb
Notes: Some important Lineage Markers :
T cells = TCR and CD4 or CD8, CD3
B cells = BCR (surface IgM or IgG) and CD19 o B220
NK cells = NK1.1, DX5
Dendritic cells = CD11c
There are different type of immune cells. To distinguish them, rather then just rely on morphology, we can use molecular features because each cell type express specific proteins. We use these markers to identify their lineage.
Let’s look at the T cells, some express CD4, CD8. They have similar morphology but different functions. To study them separately, we stain the cells with fluorescence tagged antibodies to CD4 or CD8. Then by reading the color, we can figure out CD4 CD8 T cells.
Flow cytometry is an important tool to identify different immune cell subsets.

## Slide 3
Flow Cytometry

## Slide 5: Fluidics Schematic
Sheath
Tank
Waste
Tank
Line Pressure
Vacuum
Sample
Pressure
(Variable)
Sheath Pressure
(Constant)
Notes: Next, let’s look the inside of the cytometer. The sheath fluid comes from sheath tank, go through flow cell, then collected in waste tank. The sheath fluid is under constant pressure. On top of this sheath pressure, additional pressure is applied to the sample, so that sample can flow into the flow cell. The sample differential pressure is adjustable, that is how we control the flow rate.

## Slide 6: Flow Cell
Laser
Hydrodynamic
Focusing
From Purdue University Cytometry Laboratories
Notes: To make accurate measurement, the cells must be measured one at a time, in other words, they must travel single-file in the stream. The method to achieve this is Hydrodynamic focusing. In the flow cell, a slow-moving sample stream is injected into the faster-moving sheath stream. By surface tension and laminar flow, the sample stream is brought into a narrow faster moving stream and travel single file.

## Slide 7
Core Stream
LASER LIGHT
High flow rate
Wide core stream
Faster sample rate
More coincident events
Increased abort rate
Cells are not all excited equally

## Slide 8: Forward Scatter (FSC)

## Slide 9: Side Scatter (SSC)

## Slide 10
Side Scatter
refracted and reflected light
granularity and internal complexity
Light Source
Forward Scatter
defracted light
cell size

## Slide 11: Scatter Plot
FSC
SSC
Lymphocytes
Monocytes
Granulocytes
RBCs
Debris
Notes: Different type of cell has its unique scatter property. In this scatter plot, we can see several populations.
FSC is not a precise way to measure the size of the cell.

## Slide 12: Fluorescence
excitation
emission
Ex.
Em.

## Slide 13
PE Spectra

## Slide 14: Photons In ~ Voltage Out
PMT Voltage Input
150V-999V
Current
Linear
Amplification
Log
Amplification
Voltage
Time
Voltage
PMT
Notes: The detectors collect light and convert them to current. The current go through lin or log amp and is transformed into vol. For each event, in the end, we get a vol pulse.
The current can be amplified by the voltage applied to the detector, so the detector is also called PMT.

## Slide 15: Measurements of the Pulse
Height
Width
Area
Time
Voltage Intensity
Notes: 15

## Slide 16: Histogram
Event # | Param 1 FSC | Param2 SSC | Param 3 FITC | Param 4 PE
1 | 100 | 500 | 10 | 650
2 | 110 | 505 | 700 | 700
3 | 90 | 480 | 720 | 670
4 | 95 | 490 | 15 | 720
100 101 102 103 104
FITC
Cell Counts
Data Format: FCS files

## Slide 17: Plots
Contour Plot
Density Plot
Greyscale Density
Dot Plot

## Slide 18
Cell Sorting
Notes: This is a method to isolate HIGHLY PURE population of cells (or bacteria or particles) based on very specific combination of markers !

## Slide 19
Mouse splenocytes sorted on Aria II
32%
97%
Notes: Introduce gate

## Slide 20: Data you get
% from parent
MFI -- Median Fluorescence Intensity
Co-expression
(based on gating analysis)
What is the relative abundance of the cells ?
How much marker is on the cell ?
Population median; but can be a surrogate for single cell expression
CD4
CD8
-10
3
0
10
3
10
4
10
5
10
6
-10
3
10
3
10
4
10
5
10
6
CD4
CD8
Double

## Slide 21: Terminologies
FACS -- Fluorescence-activated cell sorting
Analyzer vs Cell sorter
Use fluorochrome name FITC, PE instead of green, red
Spillover and Compensation
Notes: Explain spillover

## Slide 22: Spillover and Compensation
FITC
FITC
PE
PE
FITC
PE
FITC alone
PE should have no signal
Real PE= Measured-Spillover
PE alone
FITC should have no signal
Real FITC = Measured-Spillover
y% FITC
x% PE

## Slide 23
Compensation
No compensation
Compensated
FITC
FITC
PE
PE
Notes: 23
This is FITC single color staining. As you can see the fitc signal spills over PE channel. By adjusting comp, we can bring this population down, so that the median of the fitc pos population is the same as neg. After the comp, fitc pos population appears more spread in pe channel. This is because the measurement error occurs at the high log range. Comp makes it more apparent. This spread makes the detection of double pos population more difficult.

## Slide 24
PE Spillover FITC very little
PE

## Slide 25
Compensation Beads
Antibody Capture Beads, save cells and get good positive staining
Not for viability dyes: PI, fixable viability dyes
Keep PMT settings same as cell samples
(exception: FSC/SSC, nothing to do with compensation)
Not for antibody titration
Not perfect, sometimes changes spectrum
Species specific
ThermoFisher Ultracomp eBeads
  Cat# 01-2222-42

## Slide 26: Positive vs. Background
“Negative”
Population
Positive
Population
Low
High
High CV
Non-specific staining
Autofluorescence
Spectral overlap
(compensation)
Notes: 26
With low bg, the positive population is well resolved.
The spread of the neg population can come from the compensation.
High bg decrease the resolution.
Hi bg can come from non-spe of the ab. So it is very important to titrate your ab. Use just enough amount to saturate the ag.

## Slide 27
LSR II

## Slide 28
Sequential laser interrogation
Laser path
FITC
PE
Notes: Laser beams are spatially separated. To assign the signals generated on different lasers to a particular cell, the variable called "laser delay" is used. Laser delay represents the time, which one particle spends on its way from primary laser to another laser.

## Slide 29
LSR II - 4 lasers, 13 colors

## Slide 30
Canto II - 2 lasers, 6 colors

## Slide 31
Canto II - 2 lasers, 6 colors
Alexa 647, TO-PRO-3
APC
Red 633 nm
PE-Cy7
PerCP-eFluor 710, PE-Cy5.5, PI, 7-AAD
PerCP-Cy5.5
PE, PI, RFP
PE
Alexa 488, Brilliant Blue 515, GFP, YFP, CFSE
FITC
Blue 488 nm
Alternative Fluorochromes
Detector
Laser
APC-Cy7
APC-H7, APC-eFluor 780, APC/Fire 750

## Slide 32
Accuri C6 - 2 lasers, 4 colors
Located at HSF II, S107, Dr. Civin lab.
Min Jung Kim, mjkim@som.umaryland.edu, 6-1218

## Slide 33
Accuri C6 - 2 lasers, 4 colors
Alexa 647, TO-PRO-3
APC
Red 633 nm
PerCP-eFluor 710, PE-Cy5.5, PI, 7-AAD, PE-Cy7
PerCP-Cy5.5
PE, PI, RFP
PE
Alexa 488, Brilliant Blue 515, GFP, YFP, CFSE
FITC
Blue 488 nm
Alternative Fluorochromes
Detector
Laser

## Slide 34
Cytek Aurora Spectral Cytometer
4 lasers
355, 488, 407, 640 nm
over 30 colors
violet laser blue laser red laser
Notes: It is time to go Spectral. Cytek Aurora, it has only 3 laser, but can detect over 20C, including some overlapping colors. Compensation must be horrible, right?

## Slide 36
Alexa 532
FITC
Notes: It actually uses a different approach. It uses 38 detectors to record the whole spectrum of each color. For each single color we record the spec, then use this signature to unmix them in multicolor. Yes, this is called unmixing, finally I can get away from the word compensation.
This is FITC and A532’s sepectrum, emission peak overlaps significantly, but their signature is different in other areas, we can use it to unmix.

## Slide 37
Alexa 532
FITC
FITC and Alexa 532 unmixed
Notes: Do not expect magic here, population still spread out a little, but consider these two colors are not even possible to distinguish on LSR.
A532 is actually a very good color in spectral cytometer, does not interfere with other commonly used colors.

## Slide 38
LSR II 13 color Spillover Spreading Matrix (SSM)
 | BV421 | BV510 | BV605 | BV650 | FITC | PE | PE-Dazzle | PE-Cy5 | PCP-Cy5.5 | PE-Cy7 | APC | AF700 | APC-Fire
BV421 | from\into | 0.5 | 0.6 | 0.5 | 0.3 | 0.3 | 0.1 | 0.5 | 0.6 | 0.5 | 0.3 | 0.3 | 0.1
BV510 | 0.8 |  | 5.2 | 4.8 | 1.3 | 1.3 | 0.6 | 1.0 | 0.9 | 0.8 | 1.3 | 1.2 | 1.2
BV605 | 0.5 | 0.3 |  | 6.9 | 0.5 | 2.3 | 3.1 | 1.3 | 1.9 | 1.6 | 0.6 | 0.5 | 0.8
BV650 | 0.7 | 0.0 | 2.1 |  | 0.2 | 0.3 | 0.5 | 0.7 | 1.0 | 1.0 | 0.7 | 1.4 | 0.8
FITC | 0.2 | 0.4 | 0.3 | 0.7 |  | 0.1 | 0.3 | 0.4 | 0.3 | 0.3 | 0.4 | 0.3 | 0.6
PE | 0.1 | 0.1 | 1.6 | 1.4 | 0.5 |  | 4.8 | 1.4 | 3.1 | 1.5 | 0.5 | 0.4 | 0.1
PE-Dazzle | 0.1 | 0.2 | 2.7 | 2.2 | 0.4 | 5.9 |  | 2.3 | 5.9 | 2.6 | 0.9 | 0.8 | 0.5
PE-Cy5 | 0.1 | 0.1 | 0.3 | 4.2 | 0.2 | 1.1 | 0.9 |  | 15.4 | 8.5 | 4.0 | 5.8 | 2.9
PCP-Cy5.5 | 0.4 | 0.3 | 0.8 | 3.0 | 0.7 | 0.2 | 0.3 | 2.2 |  | 3.5 | 1.2 | 3.4 | 2.1
PE-Cy7 | 0.1 | 0.1 | 0.2 | 0.3 | 0.1 | 0.3 | 0.2 | 0.3 | 0.7 |  | 0.0 | 0.2 | 1.2
APC | 0.4 | 0.4 | 0.9 | 4.2 | 0.5 | 0.3 | 0.3 | 1.9 | 3.7 | 4.3 |  | 7.8 | 3.9
AF 700 | 0.5 | 0.4 | 0.8 | 1.1 | 0.6 | 0.3 | 0.2 | 1.1 | 2.0 | 4.3 | 0.5 |  | 4.1
APC-Fire | 0.5 | 0.3 | 0.1 | 0.4 | 0.2 | 0.2 | 0.6 | 0.2 | 0.5 | 7.2 | 0.2 | 1.2 | 
Showing spillover from y to x
Notes: Reference: Nguyen, R., Perfetto, S., Mahnke, Y. D., Chattopadhyay, P., Roederer, M. 2013. Quantifying spillover spreading for comparing instrument performance and aiding in multicolor panel design. Cytometry A, 83(3): 306-315

## Slide 39
 | BV421 | BV510 | BV605 | BV650 | FITC | PE | PE/Dazzle | PE-Cy5 | PCP-Cy5.5 | PE-Cy7 | APC | AF 700 | APC-Fire
BV421 | From\into | 1.1 | 0.5 | 0.5 | 1.1 | 0.5 | 0.8 | 0.4 | 0.4 | 0.1 | 0.1 | 0.3 | 0.3
BV510 | 0.4 |  | 3.2 | 2.1 | 1.9 | 1.6 | 0.9 | 1.0 | 1.1 | 0.2 | 0.3 | 0.2 | 0.2
BV605 | 0.6 | 0.4 |  | 3.6 | 0.9 | 1.2 | 1.4 | 1.5 | 1.5 | 0.5 | 0.6 | 0.3 | 0.2
BV650 | 1.1 | 0.2 | 1.9 |  | 0.8 | 0.5 | 0.3 | 1.6 | 2.0 | 0.4 | 1.2 | 0.8 | 0.7
FITC | 0.3 | 1.1 | 0.7 | 0.5 |  | 2.7 | 1.6 | 1.1 | 0.6 | 0.3 | 0.3 | 0.1 | 0.3
PE | 0.4 | 1.3 | 2.7 | 1.7 | 0.7 |  | 4.0 | 2.8 | 1.6 | 0.7 | 0.8 | 0.6 | 0.1
PE/Dazzle | 0.2 | 0.6 | 3.1 | 2.0 | 1.0 | 3.9 |  | 3.9 | 2.5 | 1.0 | 1.3 | 0.9 | 0.2
PE-Cy5 | 0.1 | 0.3 | 0.8 | 3.4 | 0.5 | 0.8 | 1.2 |  | 4.2 | 2.3 | 2.8 | 1.9 | 1.1
PCP-Cy5.5 | 0.9 | 1.5 | 0.6 | 2.8 | 0.7 | 0.2 | 0.8 | 4.1 |  | 3.1 | 1.3 | 2.1 | 1.8
PE-Cy7 | 0.3 | 0.3 | 0.2 | 0.3 | 0.5 | 0.6 | 0.3 | 0.8 | 1.0 |  | 0.2 | 0.4 | 2.4
APC | 0.5 | 0.8 | 0.3 | 2.0 | 0.9 | 0.4 | 0.1 | 1.2 | 0.9 | 0.3 |  | 2.1 | 1.6
AF 700 | 0.4 | 0.2 | 0.3 | 0.4 | 0.9 | 0.4 | 0.5 | 0.6 | 1.0 | 0.6 | 0.6 |  | 2.5
APC-Fire | 0.3 | 0.4 | 0.4 | 0.2 | 0.2 | 0.1 | 0.5 | 0.5 | 0.6 | 0.8 | 0.4 | 0.7 | 
Aurora 13 color SSM

## Slide 40: Aurora - 23 Color Panel
Spillover Spreading Matrix (SSM)
Live/dead: 7-AAD for fresh samples
Zombie NIR for fixation after stain

## Slide 41: Stain Index:
Brightness
Width of negative
The width of the negative is a function of
  Instrument performance
  Spillover (multi-color panels)
The brightness is a function of the
  Reagent
    Antigen density, fluorochrome used.
  Instrument
    PMT gain setting, laser power
Notes: Spread is measured by a metric called SI. It was developed by David Parks at Stanford University a number of years ago, and it takes into account these two concepts. First of all, you look at the MFI and what you’re looking at there is the difference between the brightness of these two populations. So, the difference is the positive versus the negative. And this difference can be due to a variety of factors. It can be due to the fluorochrome brightness, which we talked about in the first lecture. IT can be due to the antigen density, which we talked about in the second lecture. So you can see how these concepts all come together. It can also be due to factors with respect to the instrument…the pmt voltage.
The second part of the equation, the bottom half, is due to the spread of the negative population. And the spread of the negative population is due to a number of factors including those associated with the instrument that we’ll talk about greatly, and the second half of the talk will deal with fluorescence spillover because that’s the other major source of the spread.

## Slide 42
Chart: Stain Index
| BV421 | BV510 | BV605 | BV650 | FITC | PE | PE-Dazzle594 | PE-Cy5 | PerCP-Cy55 | PE-Cy7 | APC | AF 700 | APC-Fire750
LSRII | 61.7144 | 9.3279 | 29.3459 | 34.444 | 38.7029 | 103.5244 | 49.3979 | 59.6145 | 13.8038 | 114.1399 | 23.0193 | 19.4504 | 17.5846
Aurora | 50.167 | 13.1905 | 78.278 | 104.3187 | 62.0833 | 193.5718 | 133.2586 | 277.6627 | 41.3824 | 226.1877 | 153.3945 | 97.6565 | 154.1958

## Slide 43
BD FACSAria II

## Slide 44
4 way sorting into tubes
Single cell sorting for cloning

## Slide 45
10 d
The sorted single GFP positive cell grows into a colony. GFP is lost due to transient transfection.

## Slide 46
Aria II

## Slide 49
CD34: stem cells
Gamma-H2AX:
DNA double-strand breaks
20x Magnification
Resolution: 1 um/pixel
Notes: human acute myeloblastic leukemia KASUMI-1 cell line

## Slide 50: MACSQuant® Analyzer 10
Compliance with FDA 21 CFR Part 11, ready for clinical studies
Express Modes automate analysis of flow experiments via predefined experiment settings
QC for CAR T cell production in the F.A.C.T. lab, open to other labs too.
Staff run only
3 lasers, 8 colors
Notes: Fannie Angelos Cellular Therapeutics Lab

## Slide 51
Hourly Rates
Staff assisted run, additional $60/h
* $50 set up fee for each sort
 | Accuri | Canto | LSR | Aurora | Aurora UV | FlowSight | Aria | MACSQuant
Acad. | $30 | $40 | $60 | $60 | $75 | $60 | $100 * | 120 **
Industry | X | $70 | $90 | $90 | $105 | $90 | $150 * | 190 **

## Slide 52
FlowJo dongles
PC and Mac dongles can be borrowed at no charge.
Purchase site license through IHV flow core
FCS Express 7 site license
No charge to flow core users
Email Karen for instructions
Data Analysis

## Slide 53
CVD
Marcelo Sztein
Mass Cytometry
2 Fluidigm CyTOF Helios mass cytometers
Simultaneous detection of 50 metal-labeled antibodies
Other Flow Cores
IHV
Yutaka Tagaya
BSL-3 cell sorting
FlowJo Site License

## Slide 54: iLab Online Booking
cibr.umaryland.edu

## Slide 57
Biosafety
Sorting generates cell containing aerosols
Sort BSL-1 materials at BSL-2 facility
Sort BSL-2 materials at BSL-2 enhanced facility.
Bio-Bubble hood on Aria II sorter - BSL-2 enhanced practice.
Masks, lab coat, gloves required
Hands on training, one on one.
Aurora can share screen to other users.
After training, email Karen for card access.

## Slide 58: Flow Cytometry Controls
Matching unstained cells
Single color cells
  compensation
  setting the gate
Fluorescent minus one (FMO)
Isotype controls
  CD14-PE, mouse anti-human, IgG1k
  Isotype control: IgG1k-PE
FITC
PE
Notes: 58

## Slide 59
Detector configurations on our cytometers
Fluorochromes spectrum, brightness
Multicolor panel builder
Antibody search engine, database across over 20 vendors

## Slide 60
Canto II Configuration